## Slide 1: Discrete-Event Simulation and Performance Evaluation
Chaiporn Jaikaeo (chaiporn.j@ku.ac.th)
Department of Computer Engineering Kasetsart University
Materials taken from lecture slides by Karl and Willig
Cliparts taken from openclipart.org
01204525 Wireless Sensor Networks and Internet of Things
Last updated: 2018-10-27

## Slide 2: Outline
Software installation
Discrete-event simulation concept
Introduction to SimPy
Introduction to WsnSimPy

## Slide 3: Software Installation
Run pip install in your virtual environment to download and install necessary modules
pip install simpy wsnsimpy ipython \
numpy scipy matplotlib \
jupyter pandas

## Slide 4: Discrete-Event Simulation
Simulated operations are performed as a discrete sequence of events in time
"Time" stops during event processing
Event queue (sorted by event time)
Fetch next event & update simulation time
Process event
Initial Events
new event(s)

## Slide 5: SimPy Simulator
Process-based discrete-event simulator written in Python
Simulated processes are defined as Python coroutines (i.e., generators)

## Slide 6: SimPy Example
The following code simulates cars arriving at three toll booths at random points in time
  Assuming cars' inter-arrival times are exponentially distributed, with the average inter-arrival time of 30 seconds
import numpy as np
import simpy
def booth(name,env):
count = 0
while True:
yield env.timeout(np.random.exponential(30))
count += 1
print(f"At {env.now:3.0f} seconds, car #{count} arrives at {name}")
env = simpy.Environment()
env.process(booth("Booth 1",env))
env.process(booth("Booth 2",env))
env.process(booth("Booth 3",env))
env.run(until=300)

## Slide 7: Introduction to WsnSimPy
WSN simulator based on SimPy
Implements basic Node model and simple collision-free node-to-node communication

## Slide 8: Scripting WsnSimPy
Define a subclass of wsnsimpy.Node with the following methods:
  init() – (optional) called on each node before start of the first node's process
  run() – defines each node's main process
  on_receive() – called when a node receives a message
  finish() – (optional) called on each node after simulation ends

## Slide 9: Case Study: Gossip Protocol
A source broadcasts a message to all nodes in the network
Similar to flooding, but each node decides to rebroadcast with some probability

## Slide 10: Simulation Setup
import random
import wsnsimpy.wsnsimpy as wsp
def runsim(prob,source):
sim = wsp.Simulator(until=50)
# place nodes in 100x100 grids
for x in range(10):
for y in range(10):
px = 50 + x*60 + random.uniform(-20,20)
py = 50 + y*60 + random.uniform(-20,20)
node = sim.add_node(GossipNode, (px,py))
# save simulation-wide variables in the 'sim' object
sim.gossip_prob = prob
sim.source = source
# start simulation
sim.run()
gossip.py

## Slide 11: Node Model
class GossipNode(wsp.Node):
tx_range = 100
def run(self):
if self.id == self.sim.source:
self.success = True
yield self.timeout(2)
self.broadcast()
else:
self.success = False
def broadcast(self):
if self.id == self.sim.source or random.random() <= self.sim.gossip_prob:
self.log(f"Broadcast message")
self.send(wsp.BROADCAST_ADDR)
def on_receive(self, sender, **kwargs):
self.log(f"Receive message from {sender}")
if self.success:
self.log(f"Message seen; reject")
return
self.log(f"New message; prepare to rebroadcast")
self.success = True
yield self.timeout(random.uniform(0.5,1.0))
self.broadcast()
gossip.py

## Slide 12: Running Simulation
Start Python console
Import the gossip module
Call the runsim() function
E.g., the following dialog starts the simulation with gossip probability of 0.7 and 8 as the source node
>>> import gossip
>>> gossip.runsim(0.7,8)

## Slide 13: Visualizing Simulation
WsnSimPy provides wsnsimpy_tk module to take care of visualizing transmission and receptions of messages using the Tk framework
import random
import wsnsimpy.wsnsimpy_tk as wsp
def runsim(prob,source):
sim = wsp.Simulator(
until=50,
timescale=1,
terrain_size=(600,600),
visual=True)
:
:
gossip.py

## Slide 14: Visualizing Simulation
Use Node.scene object to control animation scene
The following modification will make nodes turn bold after broadcasting and turn red after receiving
class GossipNode(wsp.Node):
:
def broadcast(self):
if self.id == self.sim.source or random.random() <= self.sim.gossip_prob:
self.log(f"Broadcast message")
self.send(wsp.BROADCAST_ADDR)
self.scene.nodewidth(self.id,3)
def on_receive(self, sender, **kwargs):
self.scene.nodecolor(self.id,1,0,0)
self.log(f"Receive message from {sender}")
if self.success:
self.log(f"Message seen; reject")
return
self.log(f"New message; prepare to rebroadcast")
self.success = True
yield self.timeout(random.uniform(0.5,1.0))
self.broadcast()
gossip.py

## Slide 15: Simulation Scenarios
Number of nodes: 100
Transmission range: 125
Gossip probabilities: 0.1 – 1.0

## Slide 16: Evaluation Metrics
Message delivery ratio (i.e., #successes/#nodes)
Total number of transmissions
Total number of receptions

## Slide 17: Fixing Random Seed
Each run yields different behaviors and results due to randomness
Make each run deterministic by setting the random seed
import random
import wsnsimpy.wsnsimpy_tk as wsp
def runsim(seed,prob,source):
random.seed(seed)
sim = wsp.Simulator(
until=50,
timescale=1,
terrain_size=(600,600),
visual=True)
:
:
gossip.py

## Slide 18: Disabling Logging and GUI
To speedup simulation, logging and visualization should be disabled
class GossipNode(wsp.Node):
tx_range = 100
def run(self):
self.logging = False
if self.id == self.sim.source:
self.success = True
yield self.timeout(2)
self.broadcast()
else:
self.success = False
:
gossip.py
def runsim(seed,prob,source):
random.seed(seed)
sim = wsp.Simulator(
until=50,
timescale=0,
terrain_size=(600,600),
visual=False)
:
gossip.py

## Slide 19: Reporting Statistics
class GossipNode(wsp.Node):
tx_range = 100
def run(self):
self.tx = 0
self.rx = 0
if self.id == self.sim.source:
self.success = True
yield self.timeout(2)
self.broadcast()
else:
self.success = False
def broadcast(self):
if self.id == self.sim.source or random.random() <= self.sim.gossip_prob:
self.log(f"Broadcast message")
self.send(wsp.BROADCAST_ADDR)
self.tx += 1
def on_receive(self, sender, **kwargs):
self.rx += 1
self.log(f"Receive message from {sender}")
if self.success:
self.log(f"Message seen; reject")
return
self.log(f"New message; prepare to rebroadcast")
self.success = True
yield self.timeout(random.uniform(0.5,1.0))
self.broadcast()
gossip.py
Nodes must keep track of how many transmissions and receptions have occurred

## Slide 20: Reporting Statistics
import random
import wsnsimpy.wsnsimpy_tk as wsp
def runsim(prob,source):
sim = wsp.Simulator(until=50,timescale=0,visual=False)
# place nodes in 100x100 grids
for x in range(10):
for y in range(10):
px = 50 + x*60 + random.uniform(-20,20)
py = 50 + y*60 + random.uniform(-20,20)
node = sim.add_node(GossipNode, (px,py))
# save simulation-wide variables in the 'sim' object
sim.gossip_prob = prob
sim.source = source
# start simulation
sim.run()
num_successes = sum([n.success for n in sim.nodes])
num_tx = sum([n.tx for n in sim.nodes])
num_rx = sum([n.rx for n in sim.nodes])
return num_successes, num_tx, num_rx
gossip.py
After simulation ended, report the collective statistics

## Slide 21: Running Simulation with Script
The following script runs simulation with different sets of parameters, then save all results in a CSV file
import csv
import numpy as np
import gossip
SEED = range(5)
PROB = np.arange(0.1,1.1,.2)
with open("results.csv","w") as out:
writer = csv.writer(out)
writer.writerow(['seed','prob','success','tx','rx'])
for seed in SEED:
print(f"Running seed: {seed}")
for prob in PROB:
success,tx,rx = gossip.runsim(seed,prob,50)
writer.writerow([seed,prob,success,tx,rx])
run.py

## Slide 22: Processing Raw Data
Raw results in the CSV file can be conveniently processed with pandas
Jupyter notebook provides a great environment for manipulating and visualizing data
Start Jupyter notebook with the command (after entering the virtual environment)
Then click New -> Python3 to create a new notebook
jupyter notebook

## Slide 23: Loading CSV file
Enter and run the following cell to load the pandas library and read simulation results into a data frame
Add reachability ratio as a new series to the data frame
The data frame should now look like:
data["ratio"] = data.success / 100
%matplotlib notebook
import pandas as pd
data = pd.read_csv("results.csv")
data

## Slide 24: Summarizing Results
DataFrame's groupby method can be used to summarize results from the same probability but across different seeds
agg = data.groupby("prob")
ratio = agg.ratio.mean()
ratio

## Slide 25: Plotting Results
The resulting summary can be plotted using the plot() method
import matplotlib.pyplot as plt
ratio.plot(style="b--")
ratio.plot(style="go")
plt.grid(True)
plt.xlabel("Gossip Probability")
plt.ylabel("Reachability Ratio")